PEJABAT BURSAR

# SENARAI SPESIFIKASI SEBUT HARGA

Untuk Kegunaan J/Kuasa

Pembukaan Tender/Sebutharga

Kod Syarikat	:	____________________

T/Tangan	:	____________________

No. Rujukan Sebut Harga	: ………………………

No. Peti Tender		: ………………………

Tarikh Tutup			:  ……………………..

______________________________________________________________________

TAJUK  :	TECHNICAL SPECIFICATION FOR THE SUPPLY, 	DELIVERY, INSTALLATION, TESTING AND COMMISSIONING OF 60 UNITS OF PERSONAL COMPUTERS FOR THE DEPARTMENT OF COMPUTER AND COMMUNICATION SYSTEM ENGINEERING, FACULTY OF ENGINEERING, UNIVERSITI PUTRA MALAYSIA, SERDANG SELANGOR DARUL EHSAN.

#### I.	OBJECTIVES

The specifications provided below are for the supply, installation and 	commissioning of 60 units Personal Computers for the Department of 	Computer and Communications System Engineering, Universiti Putra 	Malaysia.

II.	GENERAL SPECIFICATION

### SUPPLY AND DELIVERY

  - This quotataion includes the supply, freighting, delivery, installation and commissioning on site at the Faculty of Engineering, Universiti Putra Malaysia (UPM), Serdang Selangor Darul Ehsan. All testing must include as appropriate, demonstration of equipment, preparation of manuals and user instructions.

  - Supplier is requested to specify the earliest possible delivery and commissioning date. UPM reserves the right to determine the date of installation of the system.

  - UPM reserves the right to accept or to reject by extension of the period required for the delivery and/or completion of the work.

  - The supplier will be liable for fulfilling all the terms, conditions and guarantees entered into this contract.

  - The supplier is requested to justify their competency for the executing the job successfully. The supplier is required to submit the company’s past experience in handling this kind of job.

  - All government taxes, tariff, regulation and insurance cover cost pertaining to the importation, supply and delivery of the equipment shall be under the responsibility of the supplier.

  - Insurance cover costs during supply, delivery, installation and commissioning shall be borne by the supplier.

### INSTALLATION AND COMMISSIONING

  - All items of equipment shall be installed on site by the successful supplier at no extra cost to UPM.

  - The site for installation will be specified in UPM. The power supply shall be obtained from nearby wall supply point. The successful supplier shall be deemed to familiarize himself with the local electricity, water supply and environment and accordingly shall be responsible for the supply and installation, of any additional electrical devices, such as voltage stabilizers transformer, etc. if the need arises.

  - The successful supplier shall undertake to install and commission the equipment on site by a qualified personnel. All the experiments/demonstrations shall be performed and the required date be analyzed during commissioning. All cost regarding the above work shall be borne by the supplier.

  - If the work carried out in item II.B (c) is not satisfactory, UPM reserves the right not to accept the handing over. UPM reserves the right to call upon other professional parties to complete the job satisfactorily. This cost will be borne by the supplier.

  - All government regulations and procedures must be followed during the installation and commissioning work. Approval from any government authorities, wherever applicable will be under the supplier responsibility.

C.	MAINTENANCE AND WARRANTY

- The supplier must provide at least 3 years of the warranty period for all 	equipment supplied and shall quote the cost maintenance contract for each equipment after expiry of 	warranty period. The warranty period must not be less than 	ONE year from the date of commissioning.

- Details of maintenance scheme shall be outlined by the 	supplier.

- Full maintenance support for all items of equipment shall be 	available locally. The engineering support shall be provided 	by competent personnel. Supplier shall indicate how and to 	what 	extent they will assist in providing the maintenance 	support.

# SPARE PARTS

The tenderer shall state the period for which he undertakes to support for supplying all spares for the facilities, supplied by him. This support must not be less than FIVE years. The tenderer must issue a guarantee letter to 	this effect.

# MANUALS AND DOCUMENTATION

- The successful tenderer shall provide TWO sets comprising 	original and duplicates copies of the following items.

  - Operating manual of the equipment.

  - Electrical wiring and circuit diagram (if any)

  - Maintenance manual

- All documents listed shall be in English.

## F.	OTHER REQUIREMENTS

- Successful tenderer shall provide complete toolkit for 	general servicing, adjustment and repair of the equipment.

- Supplier MUST guarantee the availability of good after 	sales service for all equipment supplied.

- The computer hardware and software shall be IBM 	compatible (if applicable)

- UPM reserves the right not to consider and automatically 	reject the tenderer(s) offer which fails to show any of the 	above mention items or provide only partial solution.

- Supplier shall provide prices of the accessories being 	offered.

- The equipment purchased MUST be new. Shipping 	documents and other relevant documents shall accompany 	the equipment during delivery. Units that have been used for 	the demonstration or other purposes will not be accepted.

- Supplier shall provide presentation and demonstration of 	the proposed equipment on site at other venues agreed 	upon by both parties.

- Supplier shall install network wiring to each computer.

III. SPESIFIKASI TEKNIKAL

- ITEM:	PERSONAL COMPUTER

| BIL. | UPM SPECIFICATION | SUPPLIER’S PROPOSAL (please specify) |
| --- | --- | --- |
| 1. | Main Requirement : To Supply, Deliver, Install, Testing and Commission Computer System Universiti Putra Malaysia Location and number of the …… unit : Pejabat Bursar ……. unit Product Information : (please specify) Model : Brand : Country Manufacturer : |  |
| 2. | Operating System : Microsoft Windows 7 Profesional Pro 64bit (23 unit) Microsoft Windows XP Profesional Pro 32bit (2 unit) |  |
| 3. | Processor : Small Form Factor Desktop Intel Core i5 |  |
| 4. | Memory : 4GB DDR4 Ram |  |
| 5. | Internal drive : 1TB SATA (7200 rpm), 2 partition |  |

| 6. | Display : 18.5” LED Monitor |  |
| --- | --- | --- |
| 7. | Warranty : 3 Years Warranty (on labour/part-on site) |  |
| 8. | Keyboard & Mouse : USB Keyboard (same brand as CPU) 2 Button Optical Scroll Mouse (same brand as CPU) with Mouse Pad |  |
| 9. | Antivirus Kaspersky Internet Security or for 2 Years License McAfee Internet Security |  |
| 10. | Installation, Configuration & Training : Installation shall be done by vendor Installation & Configuration for linked printer HP and Epson (LQ-2180) |  |

1.	Sila tanda :	( (  ]	 jika memenuhi spesifikasi

( ( ] 	jika tidak memenuhi spesifikasi

    - Sekiranya terdapat aksesories tambahan, sila kemukakan keterangan spesifikasi yang lengkap secara berasingan.

3.	Borang ini hendaklah diisi dalam dua (2) salinan.

PENGESAHAN JAWATANKUASA TEKNIKAL JABATAN/PUSAT TANGGUNG JAWAB

KEAHLIAN:

| Tandatangan (Pengerusi) Nama : Jawatan : |  | Tandatangan (Setiausaha) Nama : Jawatan : |
| --- | --- | --- |
|  | Tandatangan (Ahli) Nama : Jawatan : |  |

# Text boxes

DF006/BUY

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]

[      ]